Data set III:  ‹motor imagery›

### Group information:

Department of Biomedical Engineering

Tsinghua University

Beijing, 100084, P. R. China

Supervisor: GAO Xiaorong, Ph.D. ( gxr-dea@tsinghua.edu.cn )

Team Member: JIA Wenyan, Zhao Xianghua

Counselor: GAO Shangkai, YANG Fusheng

- Description of our analysis system

Processing Flow:

- Selecting subject-specific frequency bands:  [10-12Hz]

- Filtering the signals with the bandpass filter

- Computing the energy feature of C3 and C4 for every sampling point

- Constructing feature vector (dimension=2) for every trial and for every sampling point

- Classifying by a linear discriminant analysis (LDA)

Dt is a  time-varying signed distance function (TSD).  Dt<0 (Dt>0) means that trial is classified as a left (right) hand trial..

2. Format of the data

The result is saved in a Matlab-fileformat.   testtsd.mat

This file contains the following variable:

testtsd  :   TSD curve for each trial  (each row is one trial)

The format is the same one as the input parameter d in MATLAB function-criteria.m.

PS:   Our result for the training dataset:

# Text boxes

Fig.1.  Data flow from raw EEG data to the classification result

YC4

YC3

10~12

Hz

filter

Energy

feature

XC3

XC4

eC4

LDA

Dt

10~12

Hz

filter

Energy

feature

eC3